## Slide 1: Reinforcement Learning for Robotics
github.com/ShawnHymel/workshop-reinforcement-learning-for-robotics

## Slide 2: Why Reinforcement Learning?
“SpotMini prior to going on Centre Stage” by Web Summit, used under CC BY 2.0
Pros:
Robust policies that can tackle new environments
Compute is front-loaded
Infer actions from human teachers/animators
Cons:
Non-deterministic (no guarantees)
Imprecise
Setup and simulation training time
Notes: Classical controls still used in:
industrial manipulators (precision required)
aerospace certifications (traceability and determinism required)
process control systems (PID and MPC easier to implement and offer determinism)

## Slide 3: Screen: Training Phase 1

## Slide 4: CAD to Simulator
chassis.stl
wheel_left.stl
wheel_right.stl
URDF or
MJCF file
XML descriptor
Mass and inertia information
Reference mesh files
Export
meshes
Import into simulator
Simulator
MuJoCo, Gazebo, Isaac Sim, etc.
CAD
FreeCAD, Fusion 360, SolidWorks, etc.

## Slide 5: Screen: FreeCAD and MJCF

## Slide 6: Screen: Training Phase 2

## Slide 7: Reinforcement Learning: Balance Bot
Agent
Observation
IMU:
pitch, pitch rate
Motor encoders:
left/right wheel angular velocity
Motors/actuators
Robot chassis, wheels, floor, etc.
Action
Environment
Reward
alive - (A*pitch^2) - (B*action^2) - (C*(x^2 + y^2)) - D*abs(yaw_rate)
Action
Left motor: [-1.0, 1.0]
Right motor: [-1.0, 1.0]
Bala2

## Slide 8: Reinforcement Learning: Balance Bot
Observation
IMU:
pitch, pitch rate
Estimate:
velocity, yaw rate, position, heading
Reward
alive - (A*pitch_err^2) - (B*action^2) - (C*cmd_vel^2) – (D*cmd_pos^2) – (E*heading_est^2)
Agent
Motors/actuators
Robot chassis, wheels, floor, etc.
Action
Environment
Action
Left motor: [-1.0, 1.0]
Right motor: [-1.0, 1.0]
Bala-C Plus (no encoders)

## Slide 9: Actor/Critic Agent
Actor (policy)
neural network
Action
[left_motor,
right_motor]
Critic
neural network
Predicted return
v(s)
Observation

## Slide 10: Deploy Actor
Actor (policy)
neural network
Action
[left_motor,
right_motor]
Observation

## Slide 11: Screen: CleanRL PPO

## Slide 12: Charts You Should Care About
Total actual rewards from completed episodes
Episode length (timesteps) from completed episodes

## Slide 13: Charts You Should Care About
Spread of action probabilities from actor NN. Shows how much actor is committing to actions (explore vs. exploit).
Compare critic vs. actual returns:
1.0: critic predicted perfectly
0: no better than predicting the batch average return at each timestep
Negative: critic is worse than predicting the mean
Notes: Batch average return: mean return at each timestep
Critic should be better than that…it should be able to differentiate among the different states in order to more accurately predict the state value (expected discounted return from any given state/observation)

## Slide 14: Charts You Should Care About
KL divergence: how far the policy’s action distribution has moved from the policy that collected the batch. ~0.01-0.02 is healthy.
Fraction of samples whose probability ratio (new policy vs. old) moved beyond +/-20% (the objective stops rewarding further movement). ~0.1–0.3 is healthy.
Notes: Both measure how aggressively the policy was changed during the actor update.
Not aggressive enough: need more samples/episodes (learning takes too long)
Too aggressive: could prematurely collapse policy spread (settle on exploitation too fast without exploring), and it can also degrade critic’s value estimates, which in turn degrade the actor’s updates.
Keeping the (new) policy near the rollout (old) policy keeps the batch valid for both the actor's importance correction and the critic's targets.

## Slide 15: Screen: Training Phase 3

## Slide 16: Position, Velocity, Heading Estimation
Bala-C Plus
(no encoders)
# Command leaky integration: proportional
# to forward velocity/position
cmd = 0.5 * (action[0] + action[1])
cmd_vel = 0.995 *
(cmd_vel + cmd * dt)
cmd_pos = 1.0 *
(cmd_pos + cmd_vel * dt)
# Non-leaky yaw rate integration
yaw_rate = -1 * read_gyro_y()
heading = 1.0 * (heading + yaw_rate * dt)

## Slide 17: Curriculum Learning
Train policy on easier version of task
Progressively introduce harder tasks
Similar to teaching e.g. math: arithmetic > algebra > calculus
Without it, agents often never learn or learn some unintended workaround
Art: hand-tuning stages
Automated/parallelized phases

## Slide 18: Screen: Environment

## Slide 19: Sim-to-Real Gap
Simulator
Simulation does not 100% accurately represent physical robot
  Modelling inaccuracies
  Electrical/mechanical physical variations/tolerances
  Sensor/motor noise
  Action lag time
Result: what worked in sim does not always work (nearly as well) in the real world

## Slide 20: Fixing the Sim-to-Real Gap
Perfectly model everything in simulation
  Ensures closest match between sim and reality
  Requires lots of painstaking measurements
  Requires tight tolerances on electrical/mechanical components
Post-processing
  Relatively straightforward
  Known fixes e.g. filters, boosts
  Less robust (compromise by using parts of classical control methods)
Domain randomization
  Creates a robust policy that can handle variations
  More training time
Notes: More ways: on-device learning

## Slide 21: Domain Randomization
Vary some environmental factor (e.g. on robot, in the world) each episode or each timestep
Creates robust policy that can handle similar (but not exact) tasks
Policy that figures out how to work with slight hardware variances (sim-to-real gap)
Examples:
  Starting pitch and pitch rate
  Motor gain (voltage sag, asymmetry)
  Sensor noise
  Mass and friction
  Bumps and obstacles
  Gravity (balance on uneven surfaces)

## Slide 22: Screen: Deploy

## Slide 23: Going Further
RL for Robotics video series:
youtube.com/watch?v=kGish1q_WC8
My blog posts:
shawnhymel.com/blog/
Sutton & Barto:
incompleteideas.net/book/the-book-2nd.html
Grokking Deep RL:
manning.com/books/grokking-deep-reinforcement-learning
David Silver lectures: youtube.com/watch?v=2pWv7GOvuf0&list=PLqYmG7hTraZDM-OYHWgPebj2MfCFzFObQ

## Slide 24: The End